## Slide 1
Cathey
A Fully Local Voice Smart Home Assistant EECS 6895 Final Project

## Slide 2
Motivation
▸ Commercial assistants (Alexa, Google Home) send every word to the cloud
• Privacy risk · Internet dependency · Subscription cost
▸ Goal: build a capable smart home assistant that runs entirely on-device
• No cloud · No internet · No data leaves your home
▸ Platform: Raspberry Pi 5 | Fully offline inference

## Slide 3
System Architecture
▸ STT → faster-whisper tiny.en (CPU, int8)
• Transcribes speech in ~1.2 s on Pi 5
▸ SLM → Qwen2.5-3B-Instruct Q3_K_M (llama.cpp)
• Intent classification + QA + clarification in 15–50 s
▸ TTS → Piper en_US-lessac-medium (170 WPM)
• Neural TTS, played via PipeWire to Bluetooth speaker
▸ GPIO → LED ring · Stepper motors · PWM fan

## Slide 4
Hybrid Inference Pipeline
Rule-Based Fast Path (<5 ms)
▸ Regex matching on user text
▸ Handles ~70% of direct commands
▸ turn on light · open curtain · set AC
▸ Zero LLM cost
SLM Slow Path (15–50 s)
▸ Ambiguous / feeling inputs
▸ "I feel cold" → needs_clarification
▸ General QA → answer_qa + memory
▸ Structured JSON output enforced

## Slide 5
Intent Classification
▸ Four output types: direct_command · needs_clarification · general_qa · invalid
▸ Key boundary: feelings ≠ commands
• "I feel cold" is a feeling — ask user, never infer device
• "Turn on the AC" is a command — execute immediately
▸ Enforced via system prompt + few-shot examples
• CRITICAL rule: feelings → always needs_clarification
▸ Validation layer rejects malformed SLM output before execution

## Slide 6
Four-Layer Memory Architecture
Working + Episodic
▸ Working: last 8 turns (RAM only)
▸ Episodic: ChromaDB vector store
▸ Semantically similar past interactions
▸ Retrieved as RAG context for QA
Procedural + Semantic
▸ Procedural: learned trigger→action habits
▸ "I feel cold" → close window (auto-resolved)
▸ Semantic: structured key-value prefs
▸ user_name, preferred temperature, etc.

## Slide 7
Key Design Decisions
▸ Personal facts → semantic memory, not episodic
• Vector retrieval over noisy STT caused corrupted name recall
• Key-value storage is deterministic and reliable
▸ n_ctx 2048 → 1024 + 40% shorter system prompt
• Reduces per-inference time by 20–30%
▸ Embedding model pre-warmed at startup
• Eliminates 30 s cold-start penalty on first QA call
▸ GPIO + TTS run concurrently (threading)
• Hardware action and speech overlap, saves ~1–2 s per command

## Slide 8
Devices & Demo Highlights
Hardware
▸ WS2812B 12-LED ring (SPI0)
▸ Color temp 1–5 · Brightness 3-level
▸ RGB cycle · Party mode
▸ Curtain stepper motor (ULN2003)
▸ Window stepper motor (ULN2003)
▸ PWM fan (AC simulation)
▸ 20% slow · 100% fast
Demo Commands
▸ "Turn on the light"
▸ "Make the light warmer"
▸ "Open the curtain"
▸ "I feel cold" → clarification
▸ "Set the AC to 28 degrees" → fan fast
▸ "My name is Alex" → remembered
▸ "Party time" → disco + music

## Slide 9
Performance
▸ Classification accuracy: ~85% (20-command test set, Qwen2.5-3B Q3_K_M)
▸ Rule-based fast path covers ~70% of direct commands → <5 ms
▸ SLM latency: 15–50 s (Pi 5 CPU, 4 threads, n_ctx=1024)
• Bottleneck is LLM prefill — fundamentally constrained by hardware
▸ STT latency: ~1.2 s (faster-whisper tiny.en, int8)
▸ TTS latency: ~0.5 s (Piper, PipeWire)
▸ End-to-end (rule-based): ~2 s | (SLM): ~18–55 s

## Slide 10
Conclusion
▸ Cathey shows a capable smart home assistant is achievable entirely on consumer hardware
▸ Hybrid architecture is the key insight:
• Fast deterministic rules handle the common case
• SLM handles ambiguous and conversational inputs
▸ Memory is layered by reliability:
• Vector retrieval where fuzziness is acceptable
• Key-value storage where accuracy is critical
▸ Future work: wake word detection · faster quantization · more devices